## Slide 1
Data preprocessing in R software
1) Download and extract
http://www.itqb.unl.pt/~lgafeira/aulas/
2) Open R and set the current directory to “curso metabolomica”
setwd (“C:/ data path /curso metabolomica")
getwd() # to verify the data path
3) Read all functions necessary for preprocessing:
setRepositories(graphics = getOption("menu.graphics"), ind = NULL, addURLs = character())
install.packages("speaq")
install.packages("MassSpecWavelet")
source( “readBruker.R‘”)
source( “calibr.R‘”)
source( “plotNMR.R”)
source( “norm.R”)
source(“trim.R”)

## Slide 2
Data preprocessing in R software
4) Read spectra:
data_cpmg<-readBruker (“C:/ data path /curso metabolomica/cpmg”)
5) Plot spectra:
plotNMR(data_cpmg)
plotNMR(data_cpmg,9,0) # expansion between 9 and 0 ppm
6) Calibrate spectra acoording to the formate at 8.45 ppm:
data_cpmg.calibr<-calibr(data_cpmg,x,y)

## Slide 3
7) Exclude regions of the spectra (eg. water):
plotNMR(data_cpmg.calibr,x,y) # to locate residual water peak
data_cpmg.ex<- trim(data_cpmg.calibr,x1,x2,x3,x4) # remove the water peak from the data matrix
plotNMR(data_cpmg.ex,x,y)
8) Normalization Probability Quotient Normalization (PQN):
data_cpmg.final<-norm(data_cpmg.ex,method="pqn")
9) Export data table as comma separated values format (.csv):
write.table(data_cpmg.final,file="serum_cpmg.csv",sep=",",row.names=FALSE)
Data preprocessing in R software